Assembly 1 - Worksheet
What are the main functions of the CPU?
The CPU acts as the brain of the computer. Its job is to fetch, decode and execute	instructions with its use of registers and busses.

What is the main function of the data bus? What are the three main components of a data bus, and what are their functions?
The data bus is responsible for handling the connections between registers and main	memory to allow the transfer of data and instructions between each of them.
The three components are:
- Data lines, to convey bits from one device to another
- Control lines, to determine the direction of data flow, and when each device can access the bus
- Address lines to determine the data source or destination location.

How many bits are required to address a 4M×16 main memory if
Main memory is word-addressable?
A word consists of 2 or more bytes, so at least 16 bits.
Main memory is byte-addressable?
A byte is only 8 bits.

How would the following instructions appear in the IR of MARIE? Give your answers in binary and hex.
- Load 5
  00010000000001012, 100516
- Add 5
  00110000000001012, 300516
- Halt
- 01110000000000002, 800016
Name MARIE’s seven registers, and briefly describe their functions. Explain why, in MARIE, the MAR is only 12 bits wide while the AC is 16 bits wide.
Hint: Consider the difference between data and addresses.
MARIE’s seven registers are:
- Accumulator, AC
  - A 16-bit register that holds conditional operator (e.g., “less than”) or one operand of a two-operand instruction.
- Memory Address Register, MAR
  - a 12-bit register that holds the memory address or the operand of an instruction
- Memory buffer register, MBR
  - a 16-bit register that holds data after retrieval from, or before placement in emmory
- Program counter, PC
  - a 12-bit register that holds the address of the next program instruction to be executed.
- Instruction register, IR
  - a 16-bit register which holds an instruction immediately preceding its execution
- Input register, IN
  - an 8-bit register that holds data read from an input device.
- Output register, OUT
  - an 8-bit register that holds data that is ready for the output device.
MARIE’s MAR is only 12 bits wide as it does not need to carry the opcode, only the memory address or operand. The AC needs the full 16 bits in order to store the instruction (opcode) and and data (operand).